## Slide 1
Andrew Nguyen, Bryce George, Colton Homuth, William Ross
Sponsor: Dr. Adham Atyabi
Faculty Sponsor: Mr. Bill Michael
February 26, 2021
Social Interactivity Mentor for Youth with Autism using the NAO Robot (SIMYAN)
Design Review
Notes: Bryce

## Slide 2: Project Recap
Objective:
Create a framework for the NAO robot to support future implementation of ASD treatment/intervention activities designed by medical professionals and researchers.
Social Interactivity for Youth with Autism using the NAO robot
  Core SDK
    Supports advanced social interactivity behaviors
    Framework for building Activity Modules
    Orchestrates Activity Module execution
  Social Interactive Drawing Module
    PoC Activity Module
    Guides human subject through a drawing exercise
    Incorporates social interaction
Notes: Bryce

## Slide 3: Presentation Overview
Proposal Background
Design Trade-Offs
  Hardware
  Software
Hardware Selection
Requirements Updates
Design
  Schematics and Parts
  Software
Software Progress
Project Schedule
  Schedule Updates
  Remaining Work
  Gantt Chart
Budget
Knowledge Integration
https://www.eduporium.com/media/catalog/product/cache/c687aa7517cf01e65c009f6943c2b1e9/n/a/nao-print_06_4.png
Notes: Bryce

## Slide 4: Proposal Background
System Design
  Hardware System Design
    Use of Nvidia Jetson Nano to do all real-time image processing
    Use of LiDAR depth sensor or Xbox Kinect
  Software System Design
    Using core SDK and existing functionality from NAOqi framework
Notes: Andrew

## Slide 5: Proposal Background
Test Plan
  1. Unit Testing
  2. Integration Testing
  3. Demonstration Plan
Development Strategy
Agile Development | Test Driven Development | Paired-Programming
Notes: Andrew

## Slide 6: Hardware Design Trade-Offs
Configuration | NAO (no GPU) | NAO + Jetson Nano
Pros | No additional integration needed Simplifies software No additional hardware to manage | Can handle image processing load Can handle machine learning workloads Can handle additional peripheral video/camera inputs Off-load tasks from NAO processor
Cons | Cannot handle sufficient image processing load Cannot handle additional peripheral video/camera inputs | Additional integration required Requires software to function in a distributed system Adds hardware management concerns (power, bandwidth, etc.)
Notes: Andrew

## Slide 7: Software Design Trade-Offs
Configuration | Wrap NAOqi SDK | Extend NAOqi SDK
Pros | Condense code needed for SIMYAN activity modules Improve code readability | Decreased team workload Keeping SIMYAN Core SDK simple leaves smaller region for testing and validation
Cons | Increase the size of the SIMYAN Core SDK May require development of modules that are not useful beyond current project | Less modular design Requires activity implementors to know NAOqi SDK Mixing of calls & responsibilities between SIMYAN SDK and NAOqi SDK
Notes: Andrew

## Slide 8: Hardware Selection
Need two additional pieces of hardware for design
  A depth sensor to augment NAO’s vision capabilities
  A GPU/Developer kit to handle all the image/graphics processing
Selected depth sensor: Xbox Kinect
  Existing examples of it being used with NAO robot
  Much cheaper than the other options
  Will be testing to make sure the Kinect can integrate with NAO and provide additional camera accuracy
Selected GPU: Jetson Nano
  Free from advisor Bill Michael
  4GB of ram and 128 GPU cores which will allow us to run complex vision detection algorithms
  We will be testing GPU using a separate camera feed making sure it can detect objects outside of NAO’s camera initially
Notes: Colton – (Will)

## Slide 9: Requirements Updates
Eliminated extensions
  Most extension features removed
  Automated Object Drawing Specification Generator added to core feature set
Reduced robot autonomy
  Marker collection
  Mobility
Wireless connection to Jetson Nano
  Power supply needs
Notes: Will

## Slide 10: Specification Updates
Wireless communication with Jetson Nano
  Minimum Transmission Rate: 25 Mbps
  Wifi card for Jetson Nano
  No need for GPU ”backpack”
OpenCV for object detection / tracking
  Canny Edge Detection
  GOTURN
  CSRT
Kinect integration with SIMYAN only – not strictly required for drawing activity
Notes: Will

## Slide 11: Marker Schematic
Rubber Washers
Notes: Will

## Slide 12: Whiteboard Schematic
Colored Tape
Whiteboard Surface
Notes: Will

## Slide 13: Software Design
Standalone NAO activities activated within the context of the SIMYAN Master Activity
Using STK NAO Interface
Standalone NAO activity which discovers and activates SIMYAN activities
NAO Services registered by the SIMYAN Master Activity
Notes: Bryce

## Slide 14: Software Progress
Development Tools
  Robot Jumpstarter
    A repository containing NAO/Pepper project templates, utilities for creating named projects using the templates, and ability to add custom templates
  Studio Tool Kit (STK)
    A set of python scripts which provide a simplified interface for accessing NAOqi resources
  qibuild
    A python-based command line package for bootstrapping, building, and deploying packages to the NAO robot
Created, built, and deployed a test Application
  Application template from Robot Jumpstarter
  Uses STK
  Built and deployed using qibuild
Core SDK development in progress
Notes: Bryce

## Slide 15: Remaining Work
Core SDK Development | Social Interactive Drawing Module Development
Activities Master Module B Activity Module Loader Activity Module Manager Command Recognition Manager Speech Recognition Resource Module A Advanced Motor Control Resource Module AB Advanced Computer Vision Resource Module CW Jetson Nano GPU Integration C | Drawing Activity Command Recognition A Marker Detection C Marker Collection W Marker Handling B Drawing Surface Detection C Drawable Object Loader B Object Drawing Manager CW Social Interaction Manager AB Automated Object Drawing Specification Generator BC
Integration Testing | End-to-end Testing | Final Presentation | Final Report | LEGEND
Run Integration Test Cases * Fix Failures * Re-Test Failed Cases * | Run End-to-end Test Cases * Fix Failures * Re-Test Failed Cases * | Prepare Final Presentation * Prepare Demonstration * Deliver Final Presentation * | Prepare Final Report * Deliver Final Report * | * – All A – Andrew B – Bryce C – Colton W – Will Italic – In-Progress Superscript = Primary Owner(s)
Changes:
Core SDK Extensions and Social Interactive Drawing Module Extensions Epics Dropped (consistent with scope reductions)
Automated Object Drawing Specification Generator Epic moved to Social Interactive Drawing Module Development
Notes: Bryce

## Slide 16: Schedule Updates
Sprint 1 | Sprint 2 | Sprint 3 | Sprint 4 | Sprint 5 | Sprint 6
Feb 1 - Feb 16 | Feb 22 - Mar 5 | Mar 8 - Mar 19 | Mar 24 - Apr 9 | Apr 12 - Apr 23 | Apr 26 - May 7
Design Review
Core SDK Development
Social Interactive Drawing Module Development
Integration Testing
End-to-end Testing
Final Presentation
Final Report
Notes: Bryce

## Slide 17: Gantt Chart
Core SDK Development extended through end of Sprint 2 (3/5)
Start of Drawing Module Development moved to Sprint 3 (3/8), extended through Sprint 4 (4/9)
Notes: Bryce

## Slide 18: Budget
Item | Quantity | Cost per Unit ($)
Jetson Nano GPU | 1 | 0 (borrowed from advisor Bill Michael)
Realtek RTL8187L Chipset 2000mW Wireless USB Wifi Adapter 54Mbps Card | 1 | 24
Xbox Kinect | 1 | 50
Markers | 1+ | 0 (provided by team)
Whiteboard | 1 | 0 (provided by team)
Rubber Washers | 2 | 5
Total | 84 | 
Allowance | 400 | 
Notes: Will

## Slide 19: Knowledge Integration
Agile Development
Test Driven Development
System Design and Analysis
  Problem Decomposition
  Requirement Identification
  Architecture
  Systems Engineering
Machine Learning
  Computer Vision
  Natural Language Processing
Notes: Andrew

## Slide 20: Conclusion
Deliver a solution that is extensible and will expand the existing capabilities of the NAO robot
  SIMYAN Core SDK fulfills this goal
Apart from this, we will be using our core SDK to enact a scenario involving drawing with a human
  Demonstrate functionality of Core SDK
  Demonstrate a situation that will promote social interaction between a human and NAO
Overall, we are supplementing the NAO architecture to make it more powerful and easy-to-use in future endeavors
Notes: Colton – (Andrew)

## Slide 21: Any Questions?
Notes: Bryce